## Slide 1
NATIONAL INSTITUTE OF TECHNOLOGY SILCHAR
Cachar, Assam
B.Tech. VIIIth Sem
Topic : Topology Control
Subject Code : CS-442
Subject Name : Wireless Sensor Network
Submitted By:
Subhojit Ghimire
1912160
CSE-B

## Slide 2
Topology Control – Motivation and Basic Idea
Introduction:
Wireless Sensor Networks (WSNs) consist of many small, low-cost, and power-constrained sensor nodes that are wirelessly connected to a base station or sink node. The topology of the network refers to the spatial arrangement of these nodes and the way they are interconnected.
Motivation:
Reduce energy consumption. This is accomplished by reducing the number of redundant transmissions and by controlling the transmission range of nodes in the network.
Maximize the network's efficiency and extend its lifetime. The network topology affects various aspects of WSNs, such as communication latency, energy consumption, and fault tolerance. Therefore, choosing the appropriate topology is crucial for the network's performance.
Use advanced sensors as a bridge between the physical world and the digital world.
Basic Idea:
Optimize the network architecture by making sure that all sensor nodes are connected in such a way that
  minimizes the total energy consumption of the network,
  increases the network lifetime, and
  optimises the communication.

## Slide 3
Topology Control – Options and Aspects
Options for topology control:
Algorithms such as connected dominating sets, minimum-weighted dominating sets and minimum-hop spanning tree are used to create the network topology and to optimize the transmission ranges of the nodes in the network.
Flat topology: All nodes are at the same level and communicate directly with the sink node. This topology is simple and easy to deploy but may result in high energy consumption and communication overhead. Example: bus, grid, ring and random architecture.
Hierarchical topology: The sensor nodes are organized into multiple levels, with some nodes acting as cluster heads that collect and aggregate data from other nodes. This topology reduces communication overhead and energy consumption but may introduce some latency. Examples: star and tree architecture.
Mesh topology: The sensor nodes are interconnected in a mesh network, where each node can communicate directly with its neighbours. This topology provides high fault tolerance and scalability but may result in high communication overhead.
Aspects of topology-control algorithms:
Energy efficiency: Topology-control algorithms aim to minimize energy consumption by optimizing the communication paths between nodes and reducing the number of active nodes.
Network connectivity: Topology-control algorithms aim to ensure that the network remains connected even in the presence of node failures or network partitions.
Scalability: Topology-control algorithms aim to ensure that the network can scale to accommodate large numbers of nodes while maintaining performance.
Load balancing: Topology-control algorithms aim to balance the communication load between nodes to prevent overloading some nodes and under-utilizing others.

## Slide 4
Controlling Topology in Flat Networks – Features, Complexity & Parameters
Features of a flat network topology:
It is easy to implement and manage
It has no need for routing protocols
It has low latency and high throughput
It has high broadcast traffic and network congestion
It has poor scalability and security
Complexity results for flat network topology:
The minimum number of switches required to connect n devices is n/2 (assuming each switch has two ports)
The diameter (maximum distance between any two devices) of a flat network is 2
The average distance between any two devices is 1.5
Bound critical parameters for flat network topology:
The maximum number of devices that can be connected to a single switch or hub is determined by its port density (usually 24, 48 or 96 ports)
The maximum cable length between any device and the switch or hub is determined by its transmission medium (usually 100 meters for Ethernet cables)
A common bound on the node degree is 6, which suggests that each node should communicate with exactly six neighbours to minimize energy consumption and communication overhead.

## Slide 5
Controlling Topology in Flat Networks – Example Construction and Protocol
Addressing the issues on bound critical parameters for flat topology :
The greedy forwarding algorithm can be used to reduce the communication overhead by only forwarding packets to neighboring nodes that are closer to the sink node.
Power-aware routing protocol aims to optimize energy consumption by considering the transmission power of each node when forwarding packets.
Example constructions and protocols:
To improve the fault tolerance and scalability of flat network topologies, following constructions can be done:
A star topology where all devices are connected to a central hub using Ethernet cables.
A bus topology where all devices are connected to a single cable using coaxial cables.
A link state routing protocol where each device maintains a map of the entire network topology using hello messages.
The use of multiple sink nodes to reduce the load on individual sink nodes and distribute the communication load more evenly across the network.
The use of relay nodes to help extend the network's reach and provide redundancy in case of node failures.

## Slide 6
Hierarchical Networks by Dominating Sets (HNDS) - Definition & Motivation
A hierarchical network is a type of network that is organized into layers or clusters according to some rule. Some features are:
It has a scale-free topology with hubs and low-degree nodes
It has high clustering coefficients for low-degree nodes and low clustering coefficients for hubs
It has high reliability, scalability, and cost-efficiency
A dominating set is a subset of nodes in a network such that every node is either in the subset or adjacent to a node in the subset. Some applications of dominating sets are:
Clustering nodes into groups for efficient routing and communication
Reducing interference and energy consumption
Improving network performance and security
HNDS is a network topology based on a hierarchical organization of nodes into clusters, with each cluster having a cluster head or leader. The clusters are interconnected through a dominating set of nodes that provides a backbone for the network. The goal is to create a hierarchical topology for a network that minimizes the distance between the nodes in the network.
Motivation:
Reduce the energy consumption of the network, as shorter distances require less energy for communication.
Reduce communication overhead in wireless sensor networks by organizing nodes into clusters and limiting the number of long-range communication links.
These can help to increase network lifetime, reduce interference, and improve fault tolerance.

## Slide 7
HNDS - Approximation Algorithm
Hardness Result:
The hardness result for hierarchical networks by dominating sets is that, unless P = NP, there is no polynomial-time algorithm which can find the optimal solution. This means that finding the optimal solution is computationally difficult, so approximation algorithms that can find near-optimal solutions in polynomial time are used instead.
Centralized algorithms assume global knowledge of the network topology and run on a single node. These include using connected dominating sets, minimum-weighted dominating sets, and minimum-hop spanning trees, which are used to create the network topology and to optimize the transmission ranges of the nodes in the network. For example:
  Greedy algorithm that iteratively adds nodes with maximum degree to the connected dominating set (CDS) until all nodes are dominated.
  Primal-dual algorithm that constructs a CDS based on an optimal solution to a linear programming relaxation of minimum CDS (MCDS).
Distributed algorithms assume local knowledge of the network topology and run on multiple nodes concurrently. Distributed approximation algorithms such as the Greedy Dominating Set algorithm and the Greedy Connected Dominating Set algorithm are used to create a hierarchical topology for a network in a distributed fashion. These algorithms are designed to create a hierarchical topology that minimizes the distance between the nodes in the network while also minimizing the total energy consumption of the network. For example:
  MIS-based algorithm that first finds a MIS using a randomized algorithm and then connects it using spanning trees.
  Hierarchical CDS-based algorithm that partitions the network into clusters using CDSs and then recursively applies CDSs on each cluster until reaching a single cluster.

## Slide 8
Hierarchical Networks by Clustering – Independent Sets Construction
Definition:
A hierarchical network by clustering is a type of network that is organized into groups of similar data points called clusters. Features of a hierarchical network by clustering:
It has a tree-like structure called a dendrogram that shows how clusters are nested and linked
It has different levels of granularity depending on how many clusters are chosen
It has no need for specifying the number of clusters in advance
A cluster is a subset of data points that are close to each other based on some similarity measure. Examples of similarity measures:
Euclidean distance: The straight-line distance between two points
Cosine similarity: The angle between two vectors representing two points
Jaccard similarity: The ratio of common elements to total elements in two sets representing two points
Constructing Independent Sets:
To construct the hierarchical network, an independent task-set must be defined. This task-set will define the criteria that will be used to determine which data points belong to which clusters. One approach to constructing basic independent set (IS) construction is to use maximal independent sets (MIS), which identifies a set of nodes that are not connected to each other and have the largest possible size. Another approach is to use distributed algorithms, such as the Distributed Maximal Independent Set (DMIS) algorithm, which enables nodes to locally identify their neighbours and construct independent sets.

## Slide 9
Hierarchical Networks by Clustering – Generalisation & Connecting Clusters
Generalisation and Performance Insights:
A generalization of IS construction is to use k-hop independent sets instead of 1-hop independent sets. A k-hop IS is a subset of nodes such that no two nodes are within k hops from each other. A k-hop IS construction works similarly to a basic IS construction, except that each node broadcasts its weight to its k-hop neighbours instead of 1-hop neighbours. Performance insights for IS construction are:
It is a distributed and randomized algorithm that can run on large-scale networks
It can find clusters with balanced sizes and low diameters
It can handle dynamic networks where nodes can join or leave at any time
It has low communication overhead and fast convergence
Connecting Clusters using Rotating Cluster heads Algorithm:
To keep the clusters stable, many algorithms use a technique called rotating cluster heads. This means that the cluster heads are rotated periodically, so that the same cluster heads are not always in charge of the same clusters. This helps to ensure that the clusters remain stable and that the data points in the clusters remain similar. Alternatively, other algorithms that are used to construct a hierarchical network by clustering include k-means clustering, hierarchical agglomerative clustering, and optimization-based clustering. Some more algorithms include:
Distributed Clustering and Backbone Formation (DCBF) algorithm
Adaptive Rotation of Clusters for Energy Efficiency (ARCEE) algorithm
Clustering Algorithm for Sensor Networks (CASN)

## Slide 10
Hierarchical Networks by Clustering – Multihop Clusters
Multihop Cluster: In multihop clustering, the nodes within a cluster are organized into multiple layers based on their distance from the cluster head. Each layer can act as a relay for nodes that are farther away from the cluster head, enabling multihop communication within the cluster. This can help to increase network coverage and reduce energy consumption by minimizing the use of long-range communication links.
Multiple layers of clustering: In multiple layers of clustering, clusters are organized into a hierarchy of nested clusters, with each layer having its own set of cluster heads and backbone network. This can help to increase scalability and fault tolerance by distributing the communication load and providing redundancy in case of node failures.
Passive Clustering:
Passive clustering involves the formation of clusters without requiring any sort of communication between the nodes in the cluster. Instead, the nodes automatically join the clusters that are nearest to them and form a network. Passive clustering is used to reduce the amount of energy used in the network and to improve the scalability of the network.
Several algorithms have been proposed for multihop clustering, multiple layers of clustering, and passive clustering in hierarchical networks by clustering:
Multihop Clustering Algorithm for Wireless Sensor Networks (MCWSN)
Hierarchical Clustering Algorithm for Wireless Sensor Networks (HCA-WSN)
Passive Clustering Algorithm for Wireless Sensor Networks (PC-WSN)

## Slide 11
Combining Hierarchical Topologies and Power Control
Pilot-based power control: This technique is used to create energy-efficient networks. The idea is to use a hierarchical topology to break the network up into several tiers, then use pilot-based power control to assign the power levels for each tier. The goal is to reduce the amount of energy used in the network, while still maintaining the desired performance and reliability. Pilot-based power control works by measuring the signal-to-noise ratio of the transmission links and adjusting the power levels accordingly. This helps to ensure that there is an optimal balance between the power levels required to maintain the desired performance and the amount of energy used in the network.
Ad hoc Network Design Algorithm (ANDA): A method of network topology design for ad hoc networks that uses a hierarchical network model and a genetic algorithm to optimize the network performance and cost. The idea is to divide the network into different layers of logic circuits, switches, and devices, and use a genetic algorithm to find the optimal connection scheme among them. This method can improve the network reliability, scalability, and adaptability. One algorithm for designing ad hoc networks is the Hierarchical Ad hoc Network Design (HAND) algorithm. This algorithm uses a combination of different hierarchical topologies to design an ad hoc network.
CLUSTERPOW: CLUSTERPOW is a technique used to combine hierarchical topologies in ad hoc networks. It is a distributed algorithm that builds and maintains a hierarchical network topology by combining different network topologies. CLUSTERPOW uses election techniques to select the cluster head, which is responsible for maintaining the hierarchical topology. It also uses power control techniques to optimize the network performance. Additionally, CLUSTERPOW provides mechanisms for detecting and recovering from link failure and for dynamic addition and removal of nodes. This algorithm consists of the steps- Cluster Formation, Cluster Power Assignment, Hierarchical Structure Formation, Inter-Cluster Connectivity, Redundancy.

## Slide 12
Adaptive Node Activity
Geographic Adaptive Fidelity (GAF): Adaptive node activity is a technique that reduces energy consumption by turning off some nodes that share the same functionalities. GAF is a technique used to reduce energy consumption in ad hoc wireless networks by enabling nodes to automatically enter and exit sleep states. GAF works by monitoring the density of nodes in the network and putting nodes to sleep when there are too many of them in an area. Simply speaking, GAF is a location-aware routing protocol that uses this technique by dividing the network into grids and making one node active at a time from each grid. This reduces the amount of energy used by the network as well as the data forwarding capacity of the network. When the density of nodes becomes too low, the nodes will wake up to maintain the network's connectivity. GAF is useful for reducing energy consumption in ad hoc networks, especially in environments where nodes are densely packed together.
Adaptive Self-Configuring sEnsor Networks' Topologies (ASCENT): Another example of adaptive node activity is adaptive self-configuring sensor networks’ topologies (ASCENT). This is a protocol that allows nodes to assess their connectivity and adapt their participation in the network topology based on their operating region. ASCENT uses four states for nodes: active, passive, test and sleep. Active nodes participate in data transmission, passive nodes listen but do not transmit, test nodes probe their neighbours to check connectivity, and sleep nodes turn off their radios to save energy.
Turning off nodes on the basis of sensing coverage: One more way of adaptive node activity is to turn off nodes on the basis of sensing coverage. This means that some nodes can go to sleep mode if their sensing area is already covered by other active nodes. This can save energy and prolong system lifetime without reducing sensing coverage or reliability. Different protocols use different methods to decide which nodes are redundant and how often they should wake up to check their connectivity.